Moggie Cutting list- 16 foot Cortez Melonseed
Mike Wick

This is the cutting list for building a 16 foot Cortez Melonseed. I used a bare hull as a male plug to cold-mold my hull. She is molded with two layers of 3mm occume staves, each  approximately 10 inches wide. She is built by the Ashcroft method with all planks parallel but the seams  staggered between the two layers.

1 sheet of 9mm occume plywood for keelboard, transom, forehatch, and centerboard trunk.

5 sheets of 3mm occume for cold-molding the bare hull to the fruit bowl stage.

1 sheet of 3mm occume for the cockpit coaming.

2 sheets of 5mm occume for the deck.

½ sheet of 4mm occume for watertight bulkheads at the first and last station.

3 Becton inspection ports for WT bulkheads.

8 yards of 10 oz fiberglass cloth for lining the hull,  the transom, and the centerboard trunk, both sides.

20 yards of 3” fiberglass tape.

2 yards of 8 oz Kevlar cloth for reinforcing the inside of the bilge for strength where the hull meets the trailer bunks.

5 yards of dynel fabric for covering the deck;  leftover of either dynel or fiberglass for inside the deck .

16 running feet of 5/4 by 8 spruce for building a bird’s mouth mast.

12 running feet of 2 by 4 Douglas Fir for the outwales and skeg.

Random juniper boards for inwales, deckbeams, maststep, partners, carlins.

Centerboard and rudder handed down from a british sailing dinghy

Windsurfer mast and 12 foot of 2 ½ “ diameter carbon fiber sock for building a bendy boom.

Racelite RL 390 gudgeons and pintles for rudder.

½ pint of West System 420 aluminum powder

½ pint of West System graphite powder

2 Quarts of International Epoxy Primer

1 Qt of Petit gray for topsides

1 Qt of Petit sand color for interior.

1 Qt of Sickens Cetol Light varnish.

1 Qt of VC 17 bottom paint.

1 swivel cam base block for mainsheet

1 Three part B-Bullet block and tackle for mainsheet.

2 Ronson  S20 four part block and tackle for boomvang and for raising centerboard.

2 cam cleats (small), for centerboard and boomvang.

2 cam cleat (medium), for halyards.

3 stainless steel boom bails for mainboom.

1 5/16 by 3 reefing hook for tack.

10 bronze eyestraps.

½ inch stainless steel bolt of centerboard swivel.

100 foot of 3/8 diameter for halyards.

50 foot of 5/16 for light air sheets

50 foot of 7/16 for regular sheets.